## Slide 1
STARFORTH
A Physics-Inspired Adaptive Runtime with Measured,
Zero-Variance Algorithmic Determinism
Full technical review · Robert A. James (“Captain Bob”)
Patent pending — USPTO provisional, December 2025. This session covers the full technical stack: formal model, VM physics, kernel, multi-VM fleet, security, and the bare-metal DoE campaign.

## Slide 2
AGENDA
Seven parts, roughly in dependency order
I
Formal Foundations
The mathematical model and vocabulary everything else builds on
II
VM & Physics Runtime
The 7 feedback loops, and the 90-run determinism campaign
III
LithosAnanke Kernel
Bare-metal boot, memory layout, the capsule system
IV
The Tripod
Hera / Hermes / Artemis — the multi-VM fleet and its conservation law
V
Word-Level ACL
Access control, and the campaign that found and fixed a 65% regression
VI
Cross-ISA DoE
The bare-metal determinism campaign across three CPU architectures
VII
Verification & Rigor
Isabelle/HOL proofs, negative results, and honest scope
StarForth — Technical Deep Dive
1

## Slide 3
I
Formal Foundations
The mathematical model and vocabulary everything else builds on
StarForth — Technical Deep Dive
2

## Slide 4
MOTIVATION
Why adaptation and determinism are usually incompatible
Adaptive systems (inline caches, JIT compilers, browsers) improve performance by learning execution patterns at runtime — but their internal decisions vary run to run, driven by timing-sensitive heuristics. That variance is disqualifying for systems requiring certification: medical devices, flight control, financial infrastructure.
Deterministic systems achieve certifiable reproducibility by fixing behavior at design time — sacrificing runtime adaptation entirely. The literature largely treats this as an inherent trade-off (see Related Work, academic overview deck).
Central claim: an adaptive VM can achieve 0.00% algorithmic variance across 90 experimental runs. Adaptation and determinism are not mutually exclusive.
StarForth — Technical Deep Dive
3

## Slide 5
FORMAL MODEL I
Execution frequency as a discrete-time dynamical system
Discrete-time update
f[t+1] = f[t] + Δexec[t] − Δdecay[t]
Δdecay[t] = λ · f[t] · Δt
Continuous-time form
df/dt = r(t) − λf(t)
f(t) = e^(−λt) · [f₀ + ∫₀ᵗ r(τ)e^(λτ) dτ]
λ = decay coefficient · f = per-word execution frequency (heat) · r(t) = execution rate at time t. All arithmetic is Q48.16 fixed-point — no IEEE-754 involved anywhere in the loop.
StarForth — Technical Deep Dive
4

## Slide 6
FORMAL MODEL II
Cache membership, window inference, decay inference
Hot-words cache membership
e ∈ Cache ⟺ rank(e) ≤ K, rank(e) = |{e′ : f(e′) > f(e)}| + 1
Window-width inference (Loop #5)
w* = argmin{Var(w) : w ∈ [w_min, w_current]}, subject to Levene's-test p < α (0.05)
Decay-slope inference (Loop #6)
log-linearized least squares on ln(f) = ln(f₀) − λt
Transition probability (Loop #4)
P(B|A) = count(A→B) / count(A), MLE, stored Q48.16
Convergence metric
CV = σ/μ → 0
StarForth — Technical Deep Dive
5

## Slide 7
LEXICON (1/2)
The thermodynamic-metaphor vocabulary, formally defined
Term | Meaning
Execution Heat | Per-word frequency counter; increments on execution, decays over time
Hot-Words Cache | Fixed-size cache of the K highest-heat dictionary entries
Decay Coefficient (λ) | Rate constant governing exponential heat decay
Rolling Window of Truth | Circular buffer holding recent execution history
Attractor | A recurring, bounded state-space region the system settles into
Steady-State Equilibrium | The point where heat gain and decay balance
StarForth — Technical Deep Dive
6

## Slide 8
LEXICON (2/2)
Continued
Term | Meaning
Word Transition | An observed A→B execution pair, used for pipelining prediction
Deterministic Convergence | The property that repeated runs reach the same cache configuration
Variance Inflection Point | The tick at which CV crosses a stability threshold
Levene's Test | Statistical test for equality of variances, used in window inference
Phase Space | The (heat, Δheat) coordinate space used for thermal portraits
Adaptive Heartbeat | The background tick coordinator driving all 7 loops
Full lexicon with formal/measurement/category triples: ONTOLOGY.md §III (15 terms).
StarForth — Technical Deep Dive
7

## Slide 9
II
VM & Physics Runtime
The 7 feedback loops, and the 90-run determinism campaign
StarForth — Technical Deep Dive
8

## Slide 10
FEEDBACK LOOPS (1–4)
Per-word heat tracking and prediction
1
Execution Heat
dictionary_heat_optimization.c — frequency counter per word, the substrate every other loop reads.
2
Rolling Window of Truth
rolling_window_of_truth.c — double-buffered circular buffer of execution history, adaptive sizing.
3
Linear Decay
Quiescent words lose heat linearly per tick; tick-based (not wall-clock-based) as of this session's own fix.
4
Pipelining
physics_pipelining_metrics.c — word-to-word transition prediction, speculative execution via MLE transition probabilities.
StarForth — Technical Deep Dive
9

## Slide 11
FEEDBACK LOOPS (5–7) + L8 JACQUARD
Meta-inference and fleet-wide coordination
5
Window Width Inference
inference_engine.c — Levene's test + binary chop, asks “is the current window well-matched to observed dynamics,” not “what is the true curve.”
6
Decay Slope Inference
inference_engine.c — exponential regression recovers λ from observed heat trajectories.
7
Adaptive Heartbeat
Background tick coordinator (HeartbeatState) driving all six other loops on a shared cadence.
L8 Jacquard Mode Selector — ssm_jacquard.c. A steady-state machine layered above the 7 loops, switching between 6 named modes (stable, volatile, diverse, temporal, transition, omni) based on attractor-bucket statistics. Controlled by vm->ssm_l8_state.
StarForth — Technical Deep Dive
10

## Slide 12
DICTIONARY-LOOKUP MICRO-BENCHMARK
100,000-sample study of the hot-words cache
Path | Hits | Mean latency | Min | Max
Cache | 35,640 (35.64%) | 31.543 ns | 22.0 ns | 101.0 ns
Bucket | 46,880 (46.88%) | 56.237 ns | 23.0 ns | 370.0 ns
Miss | 17,480 (17.48%) | — | — | —
1.78×
speedup (56.237 / 31.543 ns), 95% CI [1.75×, 1.81×], 99% CI [1.73×, 1.83×]
99.9%
P(speedup > 1.1×) — Bayesian Beta-Binomial posterior
<0.1%
reproducibility stdev across 3 runs (1.7820× / 1.7790× / 1.7810×)
10 of 32 cache slots (31%) auto-promoted; hottest words followed a Zipfian distribution (EXIT: 114, LIT: 101). Overhead: 256B cache array + ~4.8KB per-word metadata, <0.09% of the 5MB VM address space, ~2 CPU cycles/lookup.
StarForth — Technical Deep Dive
11

## Slide 13
THE 90-RUN DETERMINISM CAMPAIGN
3 configurations × 30 runs each
Config | Early → Late | Change | Test statistic
C_NONE (all loops off) | 10.76 → 11.45 ms | −6.4% | p > 0.10
C_CACHE (cache only, no inference) | 7.84 → 7.80 ms | +0.5% | p > 0.80
C_FULL (all 7 loops active) | 10.20 → 7.61 ms | +25.4% | t=4.23, df=28, p=0.00012
Cohen's d ≈ 5.08 for C_FULL's improvement — an unusually large effect size, consistent with a structural (not incidental) mechanism.
Determinism significance
F(29,29) → ∞, p < 10⁻³⁰ · Bayesian posterior P(H₁|data) ≈ 1 − 10⁻³⁰ (agnostic prior, likelihood ratio ≈ 10³⁰) · Statistical power at n=30, δ=0.1, σ=0.05, α=0.05: power > 0.99 — over-powered for the detection task, a methodological strength worth naming explicitly.
StarForth — Technical Deep Dive
12

## Slide 14
VARIANCE DECOMPOSITION
Separating algorithm from environment
Algorithmic variance
0.00%
Cache-decision CV across 90 runs — the system's own choices, measured directly.
Environmental variance
60–70%
Wall-clock timing CV over the same runs — CPU scheduling, thermal, other processes.
The two are statistically independent: Pearson r = 0.03, p = 0.87. Levene's test W = 0.00, p < 10⁻²⁰. This is the empirical core of the “adaptive and deterministic” claim: the algorithm's choices and the machine's noisy execution of them are decoupled.
StarForth — Technical Deep Dive
13

## Slide 15
III
LithosAnanke Kernel
Bare-metal boot, memory layout, the capsule system
StarForth — Technical Deep Dive
14

## Slide 16
BOOT SEQUENCE
M0–M7, UEFI firmware to FORTH REPL
✓
M1
Console
UART 16550 + framebuffer VT100
✓
M2
PMM
Physical memory manager (bitmap)
✓
M3
VMM
4-level x86_64 paging
✓
M4
Interrupts
IDT + APIC
✓
M5
Timer
TSC + HPET + APIC, 100Hz heartbeat
✓
M6
Heap
16MB kmalloc — present, full validation deferred
…
M7
VM Bootstrap
Capsule loading → Tripod fleet → ACL → ok> REPL
M0–M5 complete, verified via QEMU/OVMF, three-arch tested. M7.1 (current frontier): capsule birth protocol, Tripod multi-VM fleet, word-level ACL.
StarForth — Technical Deep Dive
15

## Slide 17
MEMORY LAYOUT & CAPSULE SYSTEM
Content-addressed, immutable initialization payloads
Kernel memory layout
• 16MB kernel heap (kmalloc)
• Block RAM: LBN 0–991 (1MB dedicated)
• Kernel ramdrive: LBN 2048–3071 (1MB)
• LBN 2048 = init.4th entry point
• Hosted VM: 5MB total, dictionary = first 2MB
Capsule birth protocol
1. Locate capsule by name
2. Validate XXHash64 content hash
3. Allocate VM ID
4. Execute IDENTITY (capsule code)
5. Execute PERSONALITY (block 1, ramdrive)
6. Log parity record (VM ID + hash + dict hash)
Capsule taxonomy: (m) MAMA_INIT — exactly one · (p) PRODUCTION — truth-bearing baby-VM initializers · (e) EXPERIMENT — DoE workload-only. Content-addressed via XXHash64: any mutation is detectable by construction.
StarForth — Technical Deep Dive
16

## Slide 18
IV
The Tripod
Hera / Hermes / Artemis — the multi-VM fleet and its conservation law
StarForth — Technical Deep Dive
17

## Slide 19
THREE ROLES, NO OVERLAP
Capability-based dispatch, always
H
Hera — VM-HERA=0
Governor. Spawns, manages, reaps VMs. Does not do work.
H
Hermes — VM-HERMES=1
Messenger. Moves events between VMs. Does not store anything.
A
Artemis — VM-ARTEMIS=2
Memory. Owns block storage/persistence. Does not route anything.
“If you find yourself putting event dispatch logic in Artemis, or storage logic in Hermes, or work execution logic in Hera — stop. You have the wrong VM.”
Dispatch is capability-based on work type — Block I/O → Artemis, Event emit/drain → Hermes, VM lifecycle → Hera. There is no routing algorithm, and never “send to the hottest VM.”
StarForth — Technical Deep Dive
18

## Slide 20
HERMES — MESSENGER DETAIL
Point-to-point messages, PubSub channels
Message node — 8 cells
type · sender · recipient · payload · heat (Q48.16) · sequence · channel-ptr · reserved
Compudynamic lifecycle: born hot (full heat) → cools each heartbeat tick → ACK = clean death, K redistributed → NACK = requeue, reduced heat → TTL expiry = reaped, K rebalanced.
Channels — 6-cell node
One permanent COMMON channel (negotiation only). Ephemeral channels: born hot, reaped cold, owner = always the responder. Negotiation: request on COMMON → accept → owner creates channel → business conducted → owner reaps.
Terminology note: reaping is heat-gated reclamation, not mark-and-sweep — objects free only when heat decays to zero, serialized against traffic on that object only, not stop-the-world. GC vocabulary is explicitly rejected as carrying the wrong expectations.
StarForth — Technical Deep Dive
19

## Slide 21
ARTEMIS — MEMORY DETAIL
Two-BAM design over block-addressed storage
 | Physical BAM | Logical BAM
Cells/entry | 2 | 4
Fields | LBN, free flag | LBN, heat (Q48.16), XXHash64 identity, flags
Role | Raw substrate — free/not-free only | Content-addressing, ACL records, cold capsule storage
Three planned thermal zones
• Zone 0 — Block RAM, LBN 0–991 (fastest, always present, K-floor)
• Zone 1 — Ramdrive, LBN 2048–3071 (RAM-backed, block-subsystem path)
• Zone 2 — External device (dynamic, event-driven presence)
Currently authorized scope is narrower: a single 30MB flat pool, no zones yet — the zone/migration design exists but is explicitly marked Future Material, not build-authorized without the project lead reopening it.
StarForth — Technical Deep Dive
20

## Slide 22
THE FLEET INVARIANT
K conservation across the whole Tripod
Fleet K = Σ (all VM K values) ≡ 1.0
Conserved across all three VMs at all times — a physics-style constraint enforced by the runtime, not a convention that happens to be followed. Each VM runs its own compudynamic engine internally and autonomously; no VM manages another's heartbeat.
Two roles for compudynamics — do not conflate them
Role 1 — Intra-VM physics engine: drives each VM's own adaptive heartbeat (the 7 loops + K arithmetic), fully autonomous.
Role 2 — Hera's VM-lifecycle driver: Hera observes the fleet-K picture to decide health/starvation/spawn/reap. This is lifecycle telemetry, never a dispatch mechanism — Hera does not use fleet K to route work.
StarForth — Technical Deep Dive
21

## Slide 23
V
Word-Level ACL
Access control, and the campaign that found and fixed a 65% regression
StarForth — Technical Deep Dive
22

## Slide 24
ACL ARCHITECTURE
Policy lives in FORTH, not C
Every dictionary entry carries four access-control fields, checked by a C interpreter hook but governed entirely by FORTH policy in ACL.4th — zero policy logic in C.
Field | Purpose
acl_ttl | Time-to-live for the word's access grant
acl_allow | Allow/deny bitmask
acl_mode | STRICT / TTL / PINNED
acl_pinned | One-way pin — inheritance clears it, copies mode
Two console layers
ok> — emergency console (fault-handler bypass, bare REPL only)
zuse)ok> — superuser session, fully subject to ACL
Status: Phases 1–7 of 8 complete (C infrastructure, FORTH policy layer, zuse bootstrap superuser, Isabelle proof stubs, kernel parity). Phase 8 — Ed25519 PKI / thumbdrive challenge-response — is the only remaining milestone.
StarForth — Technical Deep Dive
23

## Slide 25
THE ISA GAP
A naive TTL floor cost 65% on RISC architectures
ISA | Overhead (Floor=16)
amd64 | +0.080% (3 seeds identical)
aarch64 | +61.8% to +65.6%
riscv64 | +65.9% to +68.1%
Root cause: amd64 runs ~5× faster under TCG emulation, so the same workload leaves words “cold” on RISC targets — never crossing the TTL floor, forcing repeated cold-path rechecks. Model: overhead(F) ≈ 12/(F+12), giving 43% at F=16.
Raising the floor to 256 cut RISC overhead 16× (to +3.96%/+4.45%) — better, but still non-trivial. This motivated a structural fix, not a bigger constant.
StarForth — Technical Deep Dive
24

## Slide 26
ACL-RWT — THE STRUCTURAL FIX
Same compudynamic feedback topology, applied to TTL itself
ACL Rolling Window of Truth applies the same feedback shape as Loops #2+#3+#6 to the ACL TTL: start every word fully open (MAX-TTL=65535), then infer the right TTL from a per-word 8-entry ring buffer of buffered intervals.
TTL = ⌊ Ī · (256+s) / 256 ⌋, clamped to [256, 65535] — Ī = mean buffered interval, s = Q8 slope
Measured in heartbeat ticks (1 tick = 256 word executions), not wall-clock — architecture-independent by construction.
+0.0054% to +0.0088%
final 3×3 Latin square, all nine cells, CV = 0.000%
StarForth — Technical Deep Dive
25

## Slide 27
VI
Cross-ISA DoE
The bare-metal determinism campaign across three CPU architectures
StarForth — Technical Deep Dive
26

## Slide 28
CAMPAIGN SETUP
LithosAnanke under QEMU, three architectures
Architecture | Emulation target | Timer
amd64 | OVMF | APIC @ 10µs
aarch64 | Cortex-A57 | Generic Timer
riscv64 | RV64GC | OpenSBI + CLINT
30
replicates × 16-config DoE × 3 architectures = 480 runs/arch
2,349,864
total heartbeat ticks measured, fixed 10,000ns (100kHz) tick
3×
outer-replication Latin square on top of the base campaign
All three architectures use software emulation (accel=tcg) — never run concurrently, to avoid corrupting the timing signal being measured.
StarForth — Technical Deep Dive
27

## Slide 29
BASELINE RESULTS
Execution rate is architecture-invariant
Arch | Ticks | Mean exec/tick | Mean σ(exec) | Elapsed
amd64 | 261,098 | 255.98 | 1.107 | 2.611 s
aarch64 | 261,095 | 255.98 | 1.117 | 2.611 s
riscv64 | 261,095 | 255.98 | 1.117 | 2.611 s
Cross-ISA: F₂,₇₈₃₂₈₅ ≈ 0, p = 1.000 · Cross-seed ANOVA: F₂,₆ ≈ 0, p = 1.000 · CV = 0.000%
aarch64 and riscv64 produced byte-for-byte identical CSV output (MD5-matched) on the original 261,095-row run.
“The physics of the FORTH interpreter is a property of the algorithm, not the hardware.”
StarForth — Technical Deep Dive
28

## Slide 30
THE COMPUDYNAMIC BREATHING CYCLE
A discrete 5-point limit cycle, not noise
StarForth — Technical Deep Dive
29

## Slide 31
THERMAL PHASE PORTRAIT
Heat h_n vs. Δh_n, all three architectures
StarForth — Technical Deep Dive
30

## Slide 32
TIMER-HARDWARE DIVERGENCE
Attractor-neutral — a calibration residual, not a bug
A clean aarch64 re-run diverged from riscv64 in heat columns only (hot_word_count, avg_word_heat_q48) from tick 34,001 onward — while every attractor metric (execution rate, window width, temporal trust, timing variance) stayed identical.
Interpretation: heat carries small run-to-run noise, but the attractor itself does not — the dynamics that matter for the determinism claim are unaffected.
H ∈ {667664, 667777, 667881} across three replications, all p < 2.2×10⁻¹⁶
x86-64 APIC emulation leaves a measurable calibration residual (t̄ = 0.9947, σ̄² = 9.5×10⁻³) that ARMv8's Generic Timer and RISC-V's CLINT don't share — attributed to timer hardware, not the algorithm. amd64 differs by only 3 rows total, from APIC scheduling — no effect on any headline statistic.
StarForth — Technical Deep Dive
31

## Slide 33
VII
Verification & Rigor
Isabelle/HOL proofs, negative results, and honest scope
StarForth — Technical Deep Dive
32

## Slide 34
FORMAL VERIFICATION
24 Isabelle/HOL theory files
Loop correctness (8)
StarForth_Base, Loop1_Heat … Loop7_Heartrate
Word-category correctness (5)
Arithmetic, Stack, Logical, Memory, Return-Stack Words
System properties (6)
Q48_16, Correctness, Concurrent, Transition, Mutex, +1
ACL invariants (5)
Pin-Monotone, Inherit-Clears-Pin, TTL-Bounded, Emergency-Bypass, No-Escalation
Build: isabelle build -D proof/. Explicit scope caveat, stated by the project itself: full mechanized proof of all 7 feedback loops is not yet complete — partial proofs are in progress.
StarForth — Technical Deep Dive
33

## Slide 35
NEGATIVE RESULTS
15 catalogued failure modes, published alongside the successes
Condition | Effect
Random-timer-driven control flow | CV rises to ~15%, no convergence — explicit scope boundary, no mitigation
I/O-bound workloads | ≤2% improvement; net degradation from ~5% overhead
Window size 10 (vs. default 4096) | R² < 0.5, unstable
Decay slope λ=10.0 (vs. ≈0.001) | Cache thrashing
Thermal throttling | Runtime CV > 90%; cache-decision CV stays 0%
32 concurrent CPU-saturating processes | Runtime CV > 150%; cache-decision CV still 0%
The last two rows are the sharpest demonstration of the core claim: even under conditions that make wall-clock timing wildly unstable, the algorithm's own decisions stay exactly at 0% variance.
StarForth — Technical Deep Dive
34

## Slide 36
WHAT THIS PROJECT DOES NOT CLAIM
A standing anti-claims table, maintained alongside the results
✕
Not a physical theory — thermodynamic language is an explicit modeling metaphor, not literal physics
✕
Not global optimality — locally adaptive, not provably optimal
✕
Not AI/ML — no neural networks, gradient descent, backpropagation, training data, or reinforcement learning
✕
Not the first adaptive VM, and not claimed to be the fastest or to beat JIT compilers
✕
Not complete formal verification — partial mechanized proofs, stated openly
✕
Not proven causation beyond the tested configurations
✕
Not cross-language validated — FORTH-family interpreters only, so far
✕
Not production-ready, and StarshipOS does not yet exist as a functional system
StarForth — Technical Deep Dive
35

## Slide 37
OPEN RESEARCH QUESTIONS
Where the honest debate is
1
Does full mechanized proof coverage for all 7 loops change any of the empirical conclusions, or only formalize them?
2
How far does the validated scope extend into I/O-bound and non-deterministic-control-flow workloads?
3
Does the conservation-law framing (James Law) generalize beyond FORTH-family interpreters to other VM architectures?
4
What is the actual asymptotic behavior of dictionaries beyond ~100,000 entries, where the transition matrix currently grows quadratically?
5
How does the Tripod's capability-based dispatch model scale past three VMs, given IDX>NAME and CH-ACCEPT are currently hardcoded for exactly three?
StarForth — Technical Deep Dive
36

## Slide 38
ROADMAP
2025 → 2028
2025
The VM
Done. StarForth v3.1.0, FORTH-79 compliant, 936+ tests.
2026
The Kernel
In progress. LithosAnanke M0–M7, Tripod fleet, ACL Phase 8.
2027
Self-Hosting OS
StarshipOS — storage, networking, multitasking, self-compile.
2028
Custom Hardware
FPGA feasibility study.
StarForth — Technical Deep Dive
37

## Slide 39
Let's go deeper.
Formal volumes, DoE reports, Isabelle/HOL proofs, and the full source tree are available for review.
github.com/rajames440/StarForth · rajames440@gmail.com
Robert A. James (“Captain Bob”) · Patent pending — USPTO provisional, December 2025